## Slide 1
TECHNICAL REVIEW
OmTrackVLA on a Clearpath Ridgeback
How the person is detected, how the planner works, and how the two are joined.
r100-0160
ROS 2 Jazzy
RTX 5060 8 GB
Notes: Three questions, in order. How does the robot decide which person to follow. How does the OmTrackVLA model turn a camera frame into motion. And how are those two things connected, given that they are separate systems that were never designed to talk to each other.

## Slide 2
THE WHOLE SYSTEM ON ONE SLIDE
One camera frame, two independent answers, joined afterwards
Camera frame
+ the prompt
PART 2 · DETECTION
Grounding DINO · YOLO · BoT-SORT
ground → detect → track → verify
PART 1 · PLANNING
OmTrackVLA 0.6B
encode → align → concatenate → pool → Qwen → head
A locked box
turned into metres by depth
Eight waypoints
index 1 divided by 0.1 s
PART 3
Fusion, then the gate
then cmd_vel
Each branch is a chain, not a black box — the next slides open them up in that order. The two never meet inside a neural network; they meet in the controller, after both have produced an answer.
Notes: Keep this picture in your head. Top row is detection, bottom row is the planner, and they only come together at the teal box on the right. The small grey lines inside each branch box are the order the next slides follow, so you always know where in this picture we are.

## Slide 3
PART 1 · THE MEMORY
Thirty-one frames of history, and how it is filled
padding: copies of the earliest real frame
31 slots, 4 coarse tokens each, each preceded by its own time token
the current frame, 64 fine tokens, time index 31
Filling it
A fixed-length queue. Until 31 real frames exist, the earliest one is repeated on the left, so the sequence length the model sees never changes.
Clearing it
Wiped on a prompt change, on target loss, and on re-acquisition — so the model never reasons across a gap where it was following someone else.
What it spans
At the 2 Hz planner rate, 31 frames is about 15 seconds of scene — far longer than the 0.8 s it plans forward.
Notes: The clearing rule came from an upstream bug we inherited and fixed: without it, a new episode began with the previous episode's memory, in a different room, following a different person. On the robot the same hazard is a target change, so the buffer is wiped there too.

## Slide 4
PART 1 · OUTPUT TO MOTION
A 0.1 s waypoint command reused for up to 0.75 s
The 0.1 s of motion that waypoint 1 actually describes
t = 0
t = 0.8 s
Held for one 2 Hz control period: 0.5 s
Worst case inside the bounded reuse window: 0.75 s
Waypoints land at t = 0, 0.1, 0.2, 0.3, 0.5, 0.6, 0.7, 0.8 s — the training pipeline subsamples nine integrated steps down to eight, so the spacing is uneven. Upstream takes index 1 and divides by dt = 0.1, which is the mean velocity over the first tenth of a second. The bridge then holds that number five to seven times longer. Speed clipping and acceleration limits bound the consequence; they do not remove it.
Notes: This is the technical point I most want an opinion on. Three ways out: raise the planner rate and pay the compute, run proper pure pursuit over the whole eight-waypoint path so the horizon matches the control period, or simply select a later waypoint that really does correspond to half a second. I kept upstream parity as the safer starting point, but I do not think it is right.

## Slide 5
PART 1 · WHAT IT COSTS TO RUN
Planner work begins after target lock
The local inference server runs target detection first. While the target is SEARCHING, UNCERTAIN, or LOST, it skips OmTrackVLA visual encoding and waypoint inference and returns a zero command. A September 23 no-target dry run measured about 0.023 s per frame, versus about 0.213 s before this skip. The current target view runs near 3 Hz; the heavier planner is capped at 2 Hz after LOCKED. A cached model path can be reused for at most 0.75 s and must pass the current target and safety checks.
Notes: The local inference server runs target detection first. While the target is SEARCHING, UNCERTAIN, or LOST, it skips OmTrackVLA visual encoding and waypoint inference and returns a zero command. A September 23 no-target dry run measured about 0.023 s per frame, versus about 0.213 s before this skip. The current target view runs near 3 Hz; the heavier planner is capped at 2 Hz after LOCKED. A cached model path can be reused for at most 0.75 s and must pass the current target and safety checks.
Source: docs/PROJECT_CONTEXT.md and docs/COMPUTE_PLACEMENT_PLAN.md, 2026-09-28.

## Slide 6
PART 1 · THE INTERFACE CONTRACT
It always returns a path, and never says who it is following
What it returns
Eight waypoints, each [x, y, yaw] in the robot's local frame
Always eight, on every single forward pass
Metres and radians, unnormalised, scaled by a constant
The upstream agent takes waypoint index 1, divides by dt = 0.1 s, and uses that as the base velocity. The bridge does exactly the same thing before clipping.
What it never returns
A target identity or a track
A confidence in that target
A target-present flag
A target-lost signal
Any way to abstain — it always returns eight well-formed waypoints
With no target-present output, an empty corridor and a correctly-followed leader produce the same kind of answer. Something outside the network has to tell them apart.
Audited against upstream commit e9cb1fb. A provision for a presence signal exists in the data pipeline but its call site is commented out.
Notes: This is the slide that makes the detection half necessary. A planner that cannot abstain is a planner that will confidently drive you into a wall when the person leaves the frame. Every gate in part three exists because of the right-hand column.

## Slide 7
PART 1 · THE FINDING THAT SHAPED EVERYTHING
Changing the prompt did not reliably select the target
An identical real-camera frame was tested with instructions naming a black jacket, a white lab coat, a black chair, and even motion away from the scene. The released checkpoint produced similar forward commands. The values changed slightly, but the comparison did not demonstrate reliable selection of the named person. The local target manager therefore checks identity separately, and the controller joins a depth-localized leader with the raw OmTrackVLA proposal. This observation is one frame, not a general accuracy measurement.
Notes: An identical real-camera frame was tested with instructions naming a black jacket, a white lab coat, a black chair, and even motion away from the scene. The released checkpoint produced similar forward commands. The values changed slightly, but the comparison did not demonstrate reliable selection of the named person. The local target manager therefore checks identity separately, and the controller joins a depth-localized leader with the raw OmTrackVLA proposal. This observation is one frame, not a general accuracy measurement.
Source: docs/PROJECT_CONTEXT.md and docs/COMPUTE_PLACEMENT_PLAN.md, 2026-09-28.

## Slide 8
PART 2 · HOW DETECTION WORKS
How the target is detected and tracked
The target manager runs YOLO11n and BoT-SORT on every 3 Hz target frame so it can detect and track every person in view. While the system is searching or recovering, Grounding DINO runs once every eight target frames to connect the visual attribute in the prompt to a person. A candidate must pass the geometry, colour, and ambiguity checks before the system can lock it. After locking, the tracker and the HSV appearance gallery maintain that identity on each frame. This detection branch returns the target state, track ID, bounding box, scores, and annotated image. It never produces a velocity.
Notes: The target manager runs YOLO11n and BoT-SORT on every 3 Hz target frame so it can detect and track every person in view. While the system is searching or recovering, Grounding DINO runs once every eight target frames to connect the visual attribute in the prompt to a person. A candidate must pass the geometry, colour, and ambiguity checks before the system can lock it. After locking, the tracker and the HSV appearance gallery maintain that identity on each frame. This detection branch returns the target state, track ID, bounding box, scores, and annotated image. It never produces a velocity.

## Slide 9
PART 2 · FROM SENTENCE TO QUERY
How one instruction becomes two model inputs
The active startup instruction is “Follow the person who is holding blue basket.” OmTrackVLA receives that full sentence. The target manager removes action words, extracts “blue basket,” and asks Grounding DINO for “person.” and “blue basket.” as separate phrases. It accepts the basket only when the attribute box lies mostly inside a detected person box, is smaller than that box, and passes the blue colour check. The full instruction still reaches the released planner; the selected target box enters the local controller after inference.
Notes: The active startup instruction is “Follow the person who is holding blue basket.” OmTrackVLA receives that full sentence. The target manager removes action words, extracts “blue basket,” and asks Grounding DINO for “person.” and “blue basket.” as separate phrases. It accepts the basket only when the attribute box lies mostly inside a detected person box, is smaller than that box, and passes the blue colour check. The full instruction still reaches the released planner; the selected target box enters the local controller after inference.
Source: docs/PROJECT_CONTEXT.md and docs/COMPUTE_PLACEMENT_PLAN.md, 2026-09-28.

## Slide 10
PART 2 · WHY THE PROMPT IS SPLIT
A whole sentence made every human a match
Before — one caption
"the person who is holding a blue basket"
The word person on its own matched two basket-less people in a test image, at 0.50 and 0.39. Whoever appeared first was locked. Appearance-gated recovery then refused the genuine target, and the run sat at LOST with a stale grounding score of 0.731.
After — two phrases
"person. blue basket."
The attribute is grounded as its own phrase and must then be found on a detected person. Verified on test images: no lock when no basket is present, a correct lock on "black jacket", and a mislabelled tie rejected by the colour test.
Notes: Worth drawing the parallel out loud. Grounding DINO had the same failure mode as OmTrackVLA — the words were there and they were not doing the discriminating. The difference is that Grounding DINO exposes per-phrase boxes and scores, so the failure is observable and fixable from outside. OmTrackVLA exposes nothing.

## Slide 11
PART 2 · TRACKING EVERYONE
The detector finds every person, not only the one asked for
Detect
YOLO11n at 416 pixels, person class only, confidence 0.25. The threshold is deliberately low: a missed distractor is more dangerous than a spurious one.
Associate
BoT-SORT, with sparse optical-flow camera-motion compensation — necessary because the camera is on a moving base, so image motion is not object motion.
Describe
Each box gets a colour signature, and those same vectors are handed to BoT-SORT as its appearance features, so tracking and identity use one description.
Why track people the prompt did not ask for
Because identity is a question about competition. To know the leader is still the leader, the system has to know who else is in frame and how similar they look. Tracking only the match would leave no way to notice that a second person just became the better match — which is exactly how a follower gets handed to a stranger.
Tracker settings: match threshold 0.80, appearance threshold 0.80, proximity 0.50, track buffer 30 frames — about ten seconds at the 3 Hz detection rate.
Notes: The camera-motion compensation is easy to overlook and it is load-bearing. On a static camera, a box that moves is a person who moved. On the Ridgeback, the whole image shifts whenever the base turns, and without compensation the tracker breaks identity every time the robot rotates — which is constantly, since it is turning to follow someone.

## Slide 12
PART 2 · THE COLOUR TEST, AND WHERE IT BROKE
What happens when the prompt says “person with a bag”
If the prompt says “Follow the person with a bag,” the parser treats “bag” as the visual attribute and sends “person.” and “bag.” to Grounding DINO. The target manager checks whether each detected bag lies mostly inside a YOLO person box and is smaller than the person box. Because the prompt contains no colour word, the HSV colour test is skipped. If one person has a strong, unambiguous bag match, that candidate must remain verified for three consecutive target frames before the state becomes LOCKED. If no bag is found, or two people have similarly strong bag matches, the system stays in SEARCHING and the robot does not move.
Notes: If the prompt says “Follow the person with a bag,” the parser treats “bag” as the visual attribute and sends “person.” and “bag.” to Grounding DINO. The target manager checks whether each detected bag lies mostly inside a YOLO person box and is smaller than the person box. Because the prompt contains no colour word, the HSV colour test is skipped. If one person has a strong, unambiguous bag match, that candidate must remain verified for three consecutive target frames before the state becomes LOCKED. If no bag is found, or two people have similarly strong bag matches, the system stays in SEARCHING and the robot does not move.

## Slide 13
PART 2 · HOLDING THE IDENTITY
Why the system stores an appearance signature
The appearance signature is needed because Grounding DINO runs only occasionally, while the tracker updates every target frame. After the system selects a person, it needs a lightweight way to check that the current track still resembles the same individual and to recover that individual after a brief occlusion without switching to a nearby stranger. The code stores colour distributions from the person’s clothing and compares new observations with that gallery. A poor match changes the state to UNCERTAIN and stops motion. This protects identity between grounding passes, although people wearing similar colours can still look alike to this hand-built descriptor.
Notes: The appearance signature is needed because Grounding DINO runs only occasionally, while the tracker updates every target frame. After the system selects a person, it needs a lightweight way to check that the current track still resembles the same individual and to recover that individual after a brief occlusion without switching to a nearby stranger. The code stores colour distributions from the person’s clothing and compares new observations with that gallery. A poor match changes the state to UNCERTAIN and stops motion. This protects identity between grounding passes, although people wearing similar colours can still look alike to this hand-built descriptor.

## Slide 14
PART 2 · STATE MACHINE
How the target state controls motion
The target manager starts in SEARCHING. One candidate must pass the prompt and appearance checks for three target frames before LOCKED allows motion. If its track disappears or appearance similarity drops below 0.72, the state becomes UNCERTAIN immediately and motion stops. After eight unverified frames it becomes LOST. The original track can recover, or a freshly grounded candidate can recover if it also matches the stored appearance for three frames. LOST has no automatic timeout or identity replacement. The operator uses reset_target when a different person should be selected.
Notes: The target manager starts in SEARCHING. One candidate must pass the prompt and appearance checks for three target frames before LOCKED allows motion. If its track disappears or appearance similarity drops below 0.72, the state becomes UNCERTAIN immediately and motion stops. After eight unverified frames it becomes LOST. The original track can recover, or a freshly grounded candidate can recover if it also matches the stored appearance for three frames. LOST has no automatic timeout or identity replacement. The operator uses reset_target when a different person should be selected.
Source: docs/PROJECT_CONTEXT.md and docs/COMPUTE_PLACEMENT_PLAN.md, 2026-09-28.

## Slide 15
PART 2 · WHERE THE NUMBERS COME FROM
Defaults, engineering choices, and one observed trial
Constant | Value | Provenance
Grounding box threshold | 0.35 | Library default, unchanged
Person detector confidence | 0.25 | Set low on purpose so the tracker sees everyone, not only likely targets
Colour fraction | 0.15 | Hand-set. A live maroon shirt measured 0.055–0.081 against "brown" and was refused
Ambiguity margin | 0.08 | Hand-set. No sensitivity analysis
Appearance match | 0.72 | Hand-set. One live trial saw 0.776–0.998 through loss and recovery; two similar outfits scored 0.84 against each other
Gallery update | 0.85 | Hand-set. Only near-certain frames extend the gallery, capped at eight entries
Frames to acquire / to lose | 3 / 8 | Hand-set at 3 Hz — one second to acquire, under three to declare loss
The 0.35 grounding threshold is the Grounding DINO library default. The 0.25 person confidence was chosen to retain weak detections for tracking. The values 0.15, 0.08, 0.72, 0.85, and the 3/8 frame counts are engineering choices in the local configuration. The observed ranges come from one live trial and did not tune these values. A labelled replay dataset and sensitivity analysis are still needed.
Notes: The 0.35 grounding threshold is the Grounding DINO library default. The 0.25 person confidence was chosen to retain weak detections for tracking. The values 0.15, 0.08, 0.72, 0.85, and the 3/8 frame counts are engineering choices in the local configuration. The observed ranges come from one live trial and did not tune these values. A labelled replay dataset and sensitivity analysis are still needed.

## Slide 16
PART 3 · THE PROCESS SPLIT
How Ridgeback and Thor exchange inference data
The Ridgeback computer runs ROS 2 Jazzy in Python 3.12. It receives compressed colour images, depth, LiDAR, E-stop and deadman data. In the Thor split, the ROS bridge sends the selected JPEG and full prompt over the robot network to this project’s inference server at 192.168.131.51:18765. Thor runs target tracking near 3 Hz and the OmTrackVLA planner after target lock, capped at 2 Hz. It returns target state, annotated image, waypoint path and planner status. Ridgeback keeps depth fusion, the 20 Hz safety gate and cmd_vel. The normal launcher still uses local inference; the Thor launchers are separate, and remote arming needs an explicit second opt-in. The live Thor result remains dry-run only.
Notes: The system uses two local processes because ROS 2 Jazzy runs in Python 3.12, while OmTrackVLA and CUDA run in Python 3.9. The ROS node receives compressed colour images, depth, LiDAR, E-stop, and deadman messages, then sends the selected JPEG and the full prompt to the inference server through a length-prefixed JSON connection on 127.0.0.1:18765. On the server, target tracking runs at 3 Hz, Grounding DINO runs every eighth target frame while searching or recovering, and OmTrackVLA runs at up to 2 Hz only after the target is locked. The server returns the target state, annotated image, waypoint path, and fields that state whether the planner ran. The ROS node fuses the path with target geometry, applies the safety limits at 20 Hz, and publishes cmd_vel only when every gate passes.

## Slide 17
PART 3 · COMMAND FUSION
What “branch” means in the fusion controller
In this slide, a branch means one path through the controller’s if/else decision logic. The fusion code first checks the leader’s range and then tests whether the OmTrackVLA direction points generally toward the leader. In the worked example, the projection is +0.96, so the value is positive and the controller selects the agreement branch. That branch blends 75% of the leader direction with 25% of the model direction. A zero or negative projection selects a different branch that replaces the model direction with the leader direction, while unsafe distance cases select a stop branch. “Branch taken” therefore names the rule the controller executed. It is not a model prediction or a measured trial result.
Notes: In this slide, a branch means one path through the controller’s if/else decision logic. The fusion code first checks the leader’s range and then tests whether the OmTrackVLA direction points generally toward the leader. In the worked example, the projection is +0.96, so the value is positive and the controller selects the agreement branch. That branch blends 75% of the leader direction with 25% of the model direction. A zero or negative projection selects a different branch that replaces the model direction with the leader direction, while unsafe distance cases select a stop branch. “Branch taken” therefore names the rule the controller executed. It is not a model prediction or a measured trial result.

## Slide 18
PART 3 · FUSION RULES
Five cases, and what the robot does in each
Situation | Translation | Rotation
Leader behind the robot, or at zero range | stopped | stopped
Leader nearer than 0.9 m | stopped — it does not reverse | still turns to face the leader
Model proposal points toward the leader | 0.75 leader plus 0.25 model, renormalised | the same 0.75 / 0.25 blend of the yaw terms
Model proposal points away | replaced by the leader direction | replaced by the leader bearing term
Every case above, after fusion | speed = min(0.4 × distance error, 0.20 m/s), floored at the model's own speed or 0.04 | yaw = 0.8 × bearing, clipped to 0.35 rad/s
The model keeps a real role in one case only: when it already agrees with the leader direction, its 25% share is what bends the path around an obstacle the depth check cannot see.
A leader who walks toward the robot makes it stop and turn, not back away. Reversing on approach was judged worse than holding position with a person in front.
Notes: Row two is a deliberate asymmetry. The follow distance is a floor on approach, not a setpoint to servo to from both sides. If the leader closes on the robot, the robot yields the initiative rather than retreating into whatever is behind it, which the obstacle corridor only partly covers.

## Slide 19
WHERE THIS ACTUALLY STANDS
Verified results and remaining limits
The local suite has 62 passing tests. In a live Thor dry-run with a blue-basket holder, 93 of 187 frames were LOCKED; target depth and trajectory were valid during lock. The planner updated 31 times across 30.241 seconds of lock, about 1.03 Hz against a 2 Hz cap. One stale camera response was rejected; the 20 Hz host safety timer reached a 55.006 ms maximum interval. The E-stop remained active and no physical motion was tested. On 90 fresh Ridgeback camera frames, Thor and RTX matched every target and trajectory decision. A matched live RTX timing baseline, sustained planner cadence and armable safety checks remain open. No speedup is claimed.
Notes: The local suite has 59 passing tests. A clean restarted run used 5,403 MiB of GPU memory and published the Target Tracker view at about 3.08 Hz. Two short offline comparisons reduced locked-frame median latency from 303.8–319.1 ms to 193.2–197.6 ms with shared CUDA vision preprocessing, while preserving target states and permitted-frame counts. Live latency distributions and sustained planner cadence are still unmeasured. In a blue-basket trial, the intended person was LOCKED for 15/15 initial samples, then LOST in 19 of the next 20 statuses before reacquisition. This does not establish reliable sustained following.
Source: docs/PROJECT_CONTEXT.md and docs/COMPUTE_PLACEMENT_PLAN.md, 2026-09-28.